## Slide 1: WoT Servient using SmartThings and Iotivity
May 23, 2016

## Slide 2: WoT Servient using SmartThings and Iotivity
Expose SmartThings capabilities as OCF resource types with WoT Thing Description
HTTP, CoAP, and MQTT Protocol Bindings
Uses iotivity as the resource layer
node-iotivity: existing nodejs API and binding
iot-rest-api-server: existing HTTP proxy for iotivity
New nodejs based servient shell provides a client+ server scripting API and abstract transfer layer

## Slide 3: SmartThings + Iotivity WoT Servient
Things
Things
node-iotivity
iotivity
SmartThings
Servient Shell
Scripts
Handlers
Thing Description
WS
HTTP
CoAP
MQTT
Things
iot-rest-api-server
Client - Consumes
Server - Exposes
HTTP
CoAP

## Slide 4: Some Questions
What does a SmartThings TD look like?
What does a SmartThings/OCF Resource Type look like?
Can iotivity expose Thing Descriptions?
How does the action collection pattern work?
How does the subscription pattern work?

## Slide 5: Mapping SmartThings Capabilities
W3C WoT Thing Descriptions
  WoT Thing models a SmartThings Thing, at the device level
  Capability-level granularity would be better for applications and security
OCF Resource Types and Collections
  Attributes and Commands mapped using the WoT Interaction model and abstract transfer binding
  https://github.com/connectIOT/iotivity-servient/blob/master/docs/abstract-transfer.pdf
  Resource Directory + device bridge architecture

## Slide 6: Use case for SmartThings Models
IoTivity SmartThings Bridge
A SmartThing is a collection of Capabilities
Each Capability has a model
Discover SmartThings Things and construct IoTivity resource instances from capabilities
Map the W3C WoT Interaction model in RAML, customize the json-schema payloads for Capability types

## Slide 7: Modeling SmartThings Capabilities
Use oneiota to create a canonical model for mapping an abstract SmartThings Capability using the WoT Interaction Model
Create application capability types by customizing payloads using json-schema and derived models
Use WoT Thing Descriptions and RAML Capability Models to construct instances

## Slide 8: Modeling Process
Map ST Capabilities to Thing Descriptions
Compose Thing TDs from the Capability TDs
Capability TD hrefs point to action, event, and property instances exposed by IoTivity
IoTivity exposes devices as collections of Capability models, each containing resources representing WoT properties, actions, and events
Capability types differ only by payload schema and identifier values

## Slide 9: OCF WoT Device Bridge
Devices are registered in /oic/res/, with rich links to collections of Capabilities
Capabilities are composed of OCF resource types that model WoT TD entities according to the proposed protocol binding and workflows
  atl.wot.property
  atl.wot.action
  atl.wot.event
  atl.wot.actioninstance
  atl.wot.subscription

## Slide 10: SmartThings OCF Device Bridge Mapping to Thing Description
Capability
Capability
Capability
Device
SmartThings Devices
Device
Device
Device
Capability
Capability
Capability
Capability
Property
Property
Actions
Event
Property
Property
Actions
Event
WoT Thing Description
/oic/res/
Device
Collection
Capability
Collection
IoTivity